## Slide 1
email: pascal.claquin@unicaen.fr
1BOREA (MNHN CNRS) - CREC – Station Marine Luc-Sur-Mer – Université de Caen Normandie
2IFREMER LERN & Centre de Brest
P. Claquin1, L. Serre1 O. Jolly 1F. Jacqueline2, M. Navon1, L. Chasselin, G. Izabel, L. Quemener2, D. Lemeille1, JP Lehodey1,, M. Repecaud2
Couplage d’approches d’observation fonctionnelle de la Baie de Seine
Thèse de Léon Serre- Fredj

## Slide 2
Site SMILE – Baie de Seine
(English Channel) since June 2016
Seine estuary
J. Fauchot / B. Leroy

## Slide 3
20 m depth max – Macrotidal system : tidal range 8 m
Energy is supplied by
  - solar energy
  - waves and swell energy (GEPS techno)
  fuel cell (with methanol) is used as a backup.
Sub-surface measurements
Depth measurements
Depth station
-Temperature, salinity, dissolved O2, turbidity, fluorescence (FFU), Meteorological parameters, PAR (every 20 min)
-Nutrients (OPUS sensor and WIZ sensor (when it works..))
- Fast Repetition Rate Fluorometer to estimate primary productivity
-Temperature, salinity, turbidity, fluorescence (FFU), ADCP

## Slide 5
Capteur OPUS
Capteur WIZ

## Slide 8
Indicateur DCE - Chla
Indicateur DCE - Chla

## Slide 9
Application du percentile 90
Bon / très bon

## Slide 10
Biomasse = Stock – Image figée
Production = Flux de matière, énergie

## Slide 11
Estimation of phytoplankton primary productivity
Photosynthetic parameters
every 2 hours measurements are performed by using Fast Repetition Rate Fluorometer (FRRF) Act2 Chelsea Technology, UK - since March 2017.
Production / Energy curves
Fast Repetition Rate Fluorometer (FRRF) Act2 Chelsea Technology, UK
See Oxborough et al 2012 for details

## Slide 12
Photosynthetic measurements
Production/ Energy curve
Production rate of electrons by the PSII as a function of light

## Slide 13
ETRmax
Maximal electron transport rate
The slope α
Maximal light utilization efficiency
Photosynthetic measurements
Production/ Energy curve
Production rate of electrons by the PSII as a function of light

## Slide 14
Maximal electrons transport rate for the year 2018 (Claquin et al. In prep) = Maximal photosynthetic capacity of the phytoplankton

## Slide 15
Usually in literature : estimation of primary production is based on one set of data per week or per month –
Here, we have data every 2 hours
The photosynthetic capacity is highly variable during the day.

## Slide 16
H+
H+
PSII
PSI
Carbohydrates
NADPH + H+
NADP+
e-
O2 + H+
H2O
ATP
ADP+Pi
ATPase
STROMA
LUMEN
Calvin cycle
Fluorescence variation of the PSII
Production of electrons
13C
Carbon incorporation
Calvin cycle
Fd
e-
Factor ?
Photosynthetic measurements
Estimation of carbon fixation
The relationship is not linear (Napoleon & Claquin, 2012; Morelle & Claquin, 2018)

## Slide 17
Relationship between ETR(II) and carbon fixation on SMILE site as various seasons
Claquin et al, in prep.

## Slide 18
Daily primary production estimation (Claquin et al. In prep)
Integration of the production as function of the depth

## Slide 19
Integration of the production as function of the depth
If we do the same estimation only with measurements performed at noon or only performed in the morning , the picture is not the same.
Because the maximal photosynthetic capacity change during the day.
(Claquin et al. In prep)

## Slide 20
(Claquin et al. In prep)
Comparaison interannuelle en cours……
Et utilisation de ces outils pour décrire et comprendre des phénomènes à court terme

## Slide 21
Example of a bloom event – summer 2019
  - Serre et al 2021
Bloom of Lepidodinium chlorophorum (HAB species)

## Slide 22
Example of a bloom event – summer 2019
  - Serre et al (2021)
Bloom of Lepidodinium chlorophorum (HAB species) due fresh water input

## Slide 23
Example of a bloom event
  - Serre et al 2021
Bloom of Lepidodinium chlorophorum (HAB species) due fresh water input and nutrients inputs
BLOOM

## Slide 24
Example of a bloom event
  - Serre et al “almost submitted”
Bloom of Lepidodinium chlorophorum (HAB species) due fresh water input and nutrients inputs

## Slide 25
Example of a bloom event – summer 2019
  - Serre et al 2021
Crash of the bloom and of FRRF parameters

## Slide 26
Example of a bloom event – summer 2019
  - Serre et al 2021
A drop of P concentration and an increase of N/P ratio are associated to the crash of the bloom
We showed that high frequency measurements of physicochemical biological, physiological parameters allow to detect the triggers of the bloom and its fate.
WIZ sensor

## Slide 27
Bioessais : Incubations d’échantillons avec différents apports de sels nutritifs pour comprendre la réponse de la communauté phytoplanctonique / la productivité / indicateurs physiologiques
Relations : diversité / fonctions et les impacts de la modification des apports en sels nutritifs
Serre et al soumis

## Slide 28
Merci!
À bientôt à Luc sur Mer!